## Slide 1
Smart Lift
Fan Control
Automated fan control
using temperature and motion sensors
Team : SolveX
Team Members: Debroop (ECE)
Rahat (EEE)
Fahim (ECE)
Mridha (EEE)
Presented by :

## Slide 2
PROJECT INSPIRATION
Lift fans often run unnecessarily, even when the lift is empty or during cold weather.
This results in wasted electricity and reduced fan lifespan.
Rethinking Elevator Comfort and Efficiency

## Slide 3
PROJECT STATEMENT
Intelligent Fan Control for Elevators
To design and implement an intelligent system that automatically controls an elevator fan based on real-time temperature and occupancy, ensuring optimal comfort and energy savings for passengers. This system will adapt to seasonal changes and user presence.
Temperature Sensing
Monitors ambient temperature inside the elevator cabin.
Occupancy Detection
Detects presence of people without IR sensors.
Automated Fan Control
Activates/deactivates fan based on pre-set logic.

## Slide 4
PROJECT OVERVIEW
How the System Works
The system continuously monitors the elevator's internal temperature and detects motion to infer occupancy.
Below 20°C (winter)
Fan off , regardless of occupancy.
Above 30°C (summer)
Fan on, regardless of occupancy.
Between 20-30°C
Fan operates based on motion sensor.
If motion is detected, the fan turns on; otherwise, it turns off.

## Slide 5
COMPONENTS USED
Microcontroller (Arduino Uno R3)
The brain of the system, processing sensor data and controlling outputs.
Temperature Sensor (TMP36)
Measures ambient temperature accurately.
Power Supply
Detects movement to infer presence of people.
16x2 LCD Display
Shows the presence of a person and the temperature.
DC motor (2x) & H-bridge Motor Driver
Use as a prototype of fan .
PIR Motion Sensor
Use to power the motor driver and Arduino .

## Slide 6
CIRCUIT DIAGRAM
Schematic Diagram
Simplified Circuit Diagram

## Slide 7
Code Explanation
The code is structured with an infinite loop that continuously reads sensor data, applies the defined logic, and controls the fan via the relay. Key functions include:
🔧 Pin & Library Setup
• LCD initialized with control/data pins
• TMP36, PIR, and motor driver pins defined
🌡️ Thresholds & Timer
• Fan OFF < 20°C, ON > 30°C
• 3-min run duration after motion

## Slide 8
Code Explanation
⚙️ Setup Function
• LCD and hardware pins configured
🌡️ Temp Conversion
• Reads sensor value
• Converts to temperature in °C
⚡ Motor & LCD
• ON above 30°C, OFF below 20°C
• Motion-based ON within range
🎛️ Fan Logic
• Fan control via L293D
• LCD displays status & temp

## Slide 9
WORKING DEMONSTRATION
Live System
in Action
Fan activates only when the elevator is occupied
Uses sensors to detect presence and ambient temperature
Automatically adjusts fan operation based on real-time data
Turns off during idle periods or in cool conditions
Demonstrates smart, adaptive temperature control in action

## Slide 10
CHALLENGES
Challenges Faced
Sensor calibration in varying environments.
Optimizing motion sensor placement for accurate occupancy.
Power management for continuous operation.

## Slide 11
FOR FUTURE IMPROVEMENTS
Overcoming Obstacles & Next Steps
Future Improvements
Integrate humidity sensing for enhanced comfort.
Implement predictive algorithms for fan control.
Develop a mobile app for remote monitoring and control.

## Slide 12
Thank You
………….